## Slide 1
Buffalo Creek
Indian Creek
Aptakisic Creek
Seavey Drainage Ditch
Biological and Water Quality Assessment of the Upper Des Plaines Watershed
Des Plaines River Watershed Workgroup
November 15, 2018
Chris O. Yoder
Midwest Biodiversity Institute
Columbus, OH
Year 1 Rotation:
Indian, Buffalo, and Aptakisic Creeks

## Slide 2
The Development of a Biological Assessment Plan for the DuPage and Salt Creek Watersheds
DuPage-Salt Creek Work Group
March 7, 2006
Chris O. Yoder
Center for Applied Bioassessment and Biocriteria
Midwest Biodiversity Institute
Columbus, OH
A similar approach was followed for the Upper Desplaines & for the Lower Des Plaines in 2018

## Slide 3
What is a Bioassessment?
Bioassessment – a systematic assessment of the aquatic resource using biological indicators AND chemical/physical indicators in a supporting role.
Reasonably available tools and criteria exist to assess and evaluate this for all waterbody types.
Biocriteria – numerical benchmarks for determining attainment of a goal expressed in the definition of an aquatic life designated use in the state WQS.
Bioassessment is the essential implementation tool for a TALU based approach
TALU = Tiered Aquatic Life Uses
A data driven approach to WQ management

## Slide 4
Aquatic Life Uses
Definition:
A designation (classification) assigned to a waterbody based on the aquatic assemblage that can realistically be sustained given the regional reference condition and the level of protection afforded by the applicable criteria.
potential
ALUs inherently “drive” the determination of status & management responses, thus they are a critical determinant of overall program effectiveness.
This underscores the critical importance and “reach” of aquatic life uses – they influence every aspect of water quality management.

## Slide 5
Chemical – excess nutrients from urban runoff and CSOs
Physical – extensively modified stream habitat
Biological – nuisance algal growth
Energy cycling – short nutrient spirals
Treating these independently will not solve the problem.
Mill Creek – Cincinnati, OH

## Slide 6
•
Fish Assemblage
•
Macroinvertebrates
•
Periphyton
(Use Community Level Data From At Least Two)
Physical Habitat Indicators
•
Channel morphology
•
Flow
•
Substrate Quality
•
Riparian
Chemical Quality Indicators
•
pH
•
Temperature
•
Conductivity
•
Dissolved O
2
For Specific Designated Uses Add the Following:
HUMAN/WILDLIFE CONSUMPTION
Base List
:
•
Metals (in tissues)
•
Organics (in tissues)
CORE INDICATORS
AQUATIC LIFE
Base List
:
•
Ionic strength
•
Nutrients, sediment
Supplemental List
:
•
Metals (water/sediment)
•
Organics (water/sediment)
•
Chlorophyll a
RECREATIONAL
Base List
:
•
Fecal bacteria
•
Ionic strength
Supplemental List
:
•
Other pathogens
•
Organics (water/sed.)
•
Chlorophyll a
WATER SUPPLY
Base List
:
•
Fecal bacteria
•
Ionic strength
•
Nutrients, sediment
Supplemental List
:
•
Metals (water/sediment)
•
Organics (water/sed.)
•
Other pathogens
•
Chlorophyll a
Core indicators are measured routinely – independent of assessment & management questions
Supplemental indicators are added depending on designated uses, study area setting, and monitoring objectives and questions

## Slide 7
Benthic Macroinvertebrates Active Sampling Methods Examples
Net-based methods
(including kicks,
dips, jabs, sweeps,
& picks)
Picking
Grab
samplers
Scrubbing substrates
Dome
Sampler
Notes: Among the active sampling methods commonly used, there is a good mixture of qualitative and quantitative sampling methods. This will largely depend on how the sampling method is employed. First, let’s review some of the more common collection techniques used in many of these methods. When sampling substrates that can be handled (e.g., rocks, woody debris, macrophytes), macroinvertebrates may be removed by scrubbing the substrate or picking the substrate with tweezers. Net-based methods include dips, jabs, and sweeps in one or more habitat types. Net sweeping includes methods in which the habitat is disturbed prior to, or while sweeping the net to collect dislodged macroinvertebrates. The grab sampler and the dome sampler are two types of sampling devices which are normally used for quantitative assessments. Grab samplers are available in a variety of sizes and weights to meet study needs. While they have their specific applications, they cannot be used in all habitat types, and are particularly difficult to use in the collection of samples from hard substrates or in strong currents. The diver-operated dome sampler has been an effective sampling tool for use in coarse substrates in water deeper than 0.50-0.75 m. The sampler contains a battery-operated pump that moves materials dislodged by a diver into a Nitex sample bag (Cuffney 1993).

## Slide 8
IEPA methods for field collections & lab processing

## Slide 9
Fish are a widely identifiable component of aquatic systems and are valued for their recreational uses. Most species, however, are more obscure, and comprise the second most endangered group.

## Slide 10
Illinois DNR “electric seine”
MBI pulsed D.C. electrofishing methods

## Slide 11
The Qualitative Habitat Evaluation Index (QHEI)
Substrate - types, origin, quality, embeddedness
QHEI Includes Six Major Categories of Macrohabitat
Source: The Qualitative Habitat Evaluation Index (Rankin 1989)
Instream Cover – types and quantity
Channel Quality – sinuosity, development, stability
Riparian – width, quality, bank stability & quality
Pool/Run/Riffle – depth, current types, embedded-ness, morphology
Gradient – local gradient (fall per unit distance)

## Slide 12
Chemical/Physical Field Procedures
Chemical/Physical Field Procedures
Water column grab sampling
Water column grab sampling
Depth integrated sampler
Depth integrated sampler
Automatic composite samplers
Automatic composite samplers
Time-of-travel dye injection
Time-of-travel dye injection

## Slide 13
Chemical Effluent & Exposure Information
Permitted Discharges are Sampled for
Permitted Discharges are Sampled for
a Variety of Chemicals - This Provides
a Variety of Chemicals - This Provides
Data to Determine Pollutant Loads
Data to Determine Pollutant Loads
Whole Effluent Toxicity (WET) Testing
Whole Effluent Toxicity (WET) Testing
is Performed Primarily on Effluents
is Performed Primarily on Effluents
Biochemical Markers (Biomarkers) are
Biochemical Markers (Biomarkers) are
Useful for Discerning Problem
Useful for Discerning Problem
Pollutants
Pollutants
Fish Tissue Analysis Reveals
Fish Tissue Analysis Reveals
Bioaccumulative Pollutants and Risks
Bioaccumulative Pollutants and Risks
to Human and Wildlife Health
to Human and Wildlife Health

## Slide 14
Pollution survey design – geometric allocation of sampling sites with additional sites positioned in proximity to suspected sources of stress & contamination.
Each site assigned a consistent site code (e.g., 13-6).
70 sites sampled in mainstem & tributary subwatersheds in 2016.
Each sampled for biological, habitat, & water quality parameters.
Employed 3 crews over a July-October seasonal index period.
Followed IEPA methods to ensure data consistency & relevance of results.
Three year rotation initiated in 2017.
Upper Des Plaines Watershed Bioassessment
Spatial sampling design is critical for accurately detecting impairments and providing data at the same scale at which restoration is applied.

## Slide 15
Indian Creek (15)
Buffalo Creek (17)
Aptakisicn Cr. (18)

## Slide 16
Completing the Cycle of WQ Management: Managing for Environmental Results
1: Management actions
2: Response to management
3: Stressor abatement
4: Ambient conditions
5: Assimilation and uptake
6: Biological response
Administrative Indicators [permits, plans, grants, enforcement]
“Ecological Health” The Endpoint of Concern
Stressor Indicators [pollutant loads, land practices]
Exposure Indicators [pollutant conc., habitat, ecosystem process, fate & transport]
Response Indicators [biological assemblage indices, other attributes]
Indicator Levels

## Slide 17: A Data Driven Framework
Ambient M&A and other data that includes:
  Biological Assemblages (at least two)
    Evaluate biocriteria compliance
    Evidence of response to stressor types
  Water and Sediment Chemistry Data
    Compare to biocriteria based thresholds
    Compare to regional reference benchmarks
    Evaluate efficacy of current water quality criteria
  Habitat Data
    Key limiting factor to biota – can eclipse other factors
    Key determinant of use attainability
  Land Use and Flow Data
    Effects of land use on the biota can eclipse other stressors
    Effects of hydrological modifications - proxy indicators

## Slide 18
Facility | Receiving Water Body | River Mile | Latitude | Longitude | Average Flow 2016 (MGD) | Design Average Flow (MGD) | Treatment Type1 | Nutrient Removal2
Lake Co. DPW Mill Creek WWTP | Mill Creek/Des Plaines R. | 1.0/102.0 | 42°25’00”N | 87°55’40”W | 2.1 | 7.8 | AWT | M
North Shore SD Waukegan WWTP | Des Plaines R. | 98.1 | 42°22’15”N | 87°54’53”W | 22.0 | 44.0 | AWT | P
North Shore SD Gurnee WWTP | Des Plaines R. | 95.5 | 42°21’25”N | 87°55’36”W | 23.6 | 47.2 | AWT | N
Libertyville WWTP (IL0029530) | Des Plaines R. | 84.8 | 42°15’15”N | 88°56’10”W | 4.0 | 8.0 | AWT | M
Mundelein WWTP (IL0022501) | Des Plaines R. | 84.6 | 42°15’11”N | 87°50’34”W | 5.0 | 15.0 | Secondary | M
Lake Co. DPW New Town Century WWTP (IL0071366) | Des Plaines R. | 82.3 | 42°13’30”N | 87°56’15”W | 6.0 | 18.0 | AWT | M
Lake Co. DPW Des Plaines WWTP (IL0022055) | Aptaksic Cr./ Des Plaines R. | 0.8/76.4 | 42°09’47”N | 87°55’40”W | 16.0 | 51.8 | AWT | M
Lindenhurst SD WWTP (IL0020796) | Hastings Cr. | 2.8 | 42°26’01”N | 88°01’56”W | 2.0 | 5.7 | AWT | M

## Slide 19
https://cfpub.epa.gov/dmr/

## Slide 20
Notes: Sampling locations for 2009

## Slide 22
Parameter | Water Quality Criteria |  |  | Effect Thresholds |  |  |  | Non-effect Benchmarks | 
 | IL Chronic | IL Acute |  | Ohio EPA | SW Ohio | NOAA SQRT | Other | Regional Reference | IL Non-Standard
Demand Group |  |  |  |  |  |  |  |  | 
BOD5 | NA | NA | -- |  | 2.48 mg/L [HW Streams] 2.96 mg/L [WD Streams] 2.60 mg/L [BT Rivers] | -- | -- | 2.00 mg/L [HW Streams] | --
Dissolved Oxygen (D.O.) | 5.5./6.0 mg/L [7-day rolling avg.] | 3.5/5.0 mg/L [minimum] | 7.2 mg/L [HW Streams] |  | 5.32 mg/L [All Streams] | -- | -- | 6.6 mg/L [HW Streams] | --
Suspended Solids (TSS) | NA | NA | 16.0 mg/L [HW Streams] |  | 65.7 mg/L [HW Streams] 70.8 mg/L [WD Streams] 74.3 mg/L [BT Rivers] | -- | -- | 28.0 mg/L [HW Streams] | --
Nutrients Group |  |  |  |  |  |  |  |  | 
Ammonia-N (NH3-N) | 1.24 mg/L [pH 8.0/25°C] | 8.40 mg/L [pH 8.0/25°C] |  | 0.05 mg/L [HW Streams] | 0.31 mg/L [HW Streams] | -- | 0.15 mg/L [DRSCW IPS] | 0.025 mg/L [HW Streams] | --
Total Kjeldahl Nitrogen (TKN) | NA | NA |  | 0.50 mg/L [HW Streams] | 0.51 mg/L [HW Streams] 0.58 mg/L [WD Streams] 1.05 mg/L [BT Rivers] | -- | 1.00 mg/L [DRSCW IPS11] | 0.70 mg/L | --
Evaluating Chemical Results: WQC & Threshold Effects
Most will be updated via the currently ongoing IPS development

## Slide 28
Notes: pH swings for a single station from the month of June (Arlington Drive on the mainstem) Note the swing from 7.8 to 9.2 on the 18th. Clear sign of nutrient over-enrichment.

## Slide 30
Stream Nutrient Assessment Procedure (SNAP) – a “combined” criterion for nutrient effects
Benthic Chlorophyll a
Continuous D.O. – daily “flux”

## Slide 31
Habitat alteration is consistently a leading cause of biological impairment

## Slide 33
Illinois EPA Fish Index of Biotic Integrity
The end goal are biological assemblages that meet the State’s aquatic life use “biocriteria”

## Slide 34
Illinois EPA IBI Narrative Evaluations
IL General Use Attainment Threshold

## Slide 35
Notes: Sediment results for 2009

## Slide 39
A “lines-of-evidence” approach is used to assign causes & sources.
Finding Biological impairments is a first step in impaired waters listings.